## Slide 1
Andrew Stone -- Colorado State University Slide 1
Andrew Stone, Michelle Strout, Steven DiBenedetto, and Daniel Massey
May 19, 2010
Computing Frontiers
Scalable Simulation Of Complex Network Routing Policies
Colorado State University

## Slide 2
Andrew Stone -- Colorado State University Slide 2
People who study networks, want to analyze this:
Notes: Shrink image:
- Experimentally produced model of internet topology
- Nodes are ISPs (Autonomous systems)
- 35K (Actuall have this one)!!
- Researchers want to simulate routing on this topology
- Results: routing tables
- No existing work can scale to this problem
- But our work can, and has:
- Current work: Networking researchers are using this simulator to compare the resulting routing tables to actual routing tables.
- Based on this we're coming up with ideas to improve accuracy of topology and better model protocol.
- Leading to future research
"Opening a research frontier"
---------------------------------------------
Internet toplogy between domains
Simulate different protocols (BGP)
Verify models and models of policy
Each node is an autonomous system (ISP)
35K nodes
<differences come in through the edge labels>
Points to explicitly add:
- 35 K nodes
- want to simulate BGP
- Want to get routing tables BGP
Use the phrase "could not do before"

## Slide 3
Andrew Stone -- Colorado State University Slide 3
About this model:
This is a model of the internet
Experimentally produced
Nodes are autonomous systems (ISPs)
33K nodes
source: http://www.caida.org/home/
Notes: Shrink image:
- Experimentally produced model of internet topology
- Nodes are ISPs (Autonomous systems)
- 35K (Actuall have this one)!!
- Researchers want to simulate routing on this topology
- Results: routing tables
- No existing work can scale to this problem
- But our work can, and has:
- Current work: Networking researchers are using this simulator to compare the resulting routing tables to actual routing tables.
- Based on this we're coming up with ideas to improve accuracy of topology and better model protocol.
- Leading to future research
"Opening a research frontier"
---------------------------------------------
Internet toplogy between domains
Simulate different protocols (BGP)
Verify models and models of policy
Each node is an autonomous system (ISP)
35K nodes
<differences come in through the edge labels>
Points to explicitly add:
- 35 K nodes
- want to simulate BGP
- Want to get routing tables BGP
Use the phrase "could not do before"

## Slide 4
Andrew Stone -- Colorado State University Slide 4
Analyze what?
Researchers want to know:
  How accurate this modeled topology is
  how topology affects routing tables
  how policy affects
  routing tables
Notes: Shrink image:
- Experimentally produced model of internet topology
- Nodes are ISPs (Autonomous systems)
- 35K (Actuall have this one)!!
- Researchers want to simulate routing on this topology
- Results: routing tables
- No existing work can scale to this problem
- But our work can, and has:
- Current work: Networking researchers are using this simulator to compare the resulting routing tables to actual routing tables.
- Based on this we're coming up with ideas to improve accuracy of topology and better model protocol.
- Leading to future research
"Opening a research frontier"
---------------------------------------------
Internet toplogy between domains
Simulate different protocols (BGP)
Verify models and models of policy
Each node is an autonomous system (ISP)
35K nodes
<differences come in through the edge labels>
Points to explicitly add:
- 35 K nodes
- want to simulate BGP
- Want to get routing tables BGP
Use the phrase "could not do before"

## Slide 5
Andrew Stone -- Colorado State University Slide 5
Ideally, they want a simulator that:
shows resulting routing tables
can work with large topologies (30k - 100k nodes)
can work with various policies
can produce results quickly (overnight)
works with accessible hardware
Notes: Shrink image:
- Experimentally produced model of internet topology
- Nodes are ISPs (Autonomous systems)
- 35K (Actuall have this one)!!
- Researchers want to simulate routing on this topology
- Results: routing tables
- No existing work can scale to this problem
- But our work can, and has:
- Current work: Networking researchers are using this simulator to compare the resulting routing tables to actual routing tables.
- Based on this we're coming up with ideas to improve accuracy of topology and better model protocol.
- Leading to future research
"Opening a research frontier"
---------------------------------------------
Internet toplogy between domains
Simulate different protocols (BGP)
Verify models and models of policy
Each node is an autonomous system (ISP)
35K nodes
<differences come in through the edge labels>
Points to explicitly add:
- 35 K nodes
- want to simulate BGP
- Want to get routing tables BGP
Use the phrase "could not do before"

## Slide 6
Existing simulators:
  Only work with small topologies
  Have hardcoded policies
Complicating factors:
  How to specify policy?
  Policies are more than just shortest path
  O(n^2) memory requirements for routing tables
The Problem
1
3
2
To 1: 1
To 2: 1
To 4: 4
To 2: 2
To 3: 3
To 4: 2
To 1: 1
To 3: 1
To 4: 4
4
To 1: 2
To 2: 2
To 3: 3
Andrew Stone -- Colorado State University Slide 6
Notes: Why we can address this:
- RAML
- Because of mathematical properties on RAML, we can pose the simulator as an pleasantly parallel problem and we can break up the problem to reduce the O(n^2) memory bound to O(n) at any one time.

## Slide 7
MR. Sim
Our tool: MR.Sim
  Inputs topologies: specification file
  Inputs policies: Metarouting based framework
  Parallelism: embarrassingly parallel through simulation segmentation
    reduces O(n^2) memory requirements to O(n) at any one time
Andrew Stone -- Colorado State University Slide 7

## Slide 8
How a topology is modeled
Nodes = autonomous systems
Edges = connections
Edge labels describe the connection and influence policy
1
4
3
6
2
5
7
Examples of connections
c: customer connection
r: peer connection
p: provider connection
p
p
p
p
p
p
c
c
c
c
c
c
r
r
Andrew Stone -- Colorado State University Slide 8

## Slide 9
How topologies are input to Mr. Sim
Map files list the edges in the network graph and the policies (labels) that are on those edges.
1
3
2
5
4
p
p
p
p
c
c
c
c
r
r
SimpleNet.map
1 2 c
2 1 p
1 3 c
3 1 p
2 3 r
3 2 r
2 4 c
4 2 p
2 5 c
5 2 p
Andrew Stone -- Colorado State University Slide 9
Notes: Where map files come in?

## Slide 10
Routing Policies
RAML: Routing Algebra Meta Language
Andrew Stone -- Colorado State University Slide 10
Routing algebras
Composition operators
Routing algebras represent policies
RAML policies are guaranteed to converge

## Slide 11
Routing Algebras
Andrew Stone -- Colorado State University Slide 11
All about signatures and labels
Labels describe: connections
Signatures describe: routes
Signatures give routes some value
A route is: (destination, next-hop, signature)

## Slide 12
Routing Algebras
Set of possible signatures
Preference relation (partial ordering of sigs)
Set of possible labels
Label operator
Originator set (possible signatures initial routes can have)
Andrew Stone -- Colorado State University Slide 12

## Slide 13
Nodes propagate routes to neighbors. Neighbors update their routing tables based on the propagated information.
3
1
2
4
c
r
p
p
p
r
r
c
Dest | Nh | Sig
1 | 1 | C
Hey 4, I’ve got this route to 1
Dest | Nh | Sig
1 | ? | ?
Great, I’ll update my table to include that. The sig changes to R though.
Dest | Nh | Sig
1 | 2 | R
Dest | Nh | Sig
1 | 1 | R
Propagating routes
A route is: (destination, next-hop, signature) = {C, R, P} L = {c, r, p}
Signature determines how C < R < P
preferred a route is smaller is more preferred.
Andrew Stone -- Colorado State University Slide 13

## Slide 14
A route is: (destination, next-hop, signature) = {C, R, P} L = {c, r, p}
Signature determines how C < R < P
preferred a route is smaller is more preferred.
When a route is propagated it is compared against any existing routes to the same destination. The table is only updated if the new route is more preferred than the current one.
3
1
2
4
c
r
p
p
p
r
r
c
Dest | Nh | Sig
1 | ? | ?
Dest | Nh | Sig
1 | 2 | R
Dest | Nh | Sig
1 | 1 | R
Hey 4, do you want to use this route to 1?
No way, the route that way will have a signature of P! I’ll keep what I’ve got.
Dest | Nh | Sig
1 | 1 | C
Propagating routes
Andrew Stone -- Colorado State University Slide 14

## Slide 15
Mr. Sim Classes:
The framework includes the following abstract classes:
Signature
Label
PreferenceRelation
LabelOperator
NetworkReader
Algebra
Algebra is passed a PreferenceRelation, LabelOperator, and NetworkReader
Mr. Sim model’s routing algebras in a C++ framework. Users override these classes to define various properties of the algebra.
Andrew Stone -- Colorado State University Slide 15

## Slide 16
BGP Policy
FM(LP(3))
SIMSEQ(0, N-1)
RouteID()
BGP = FM(LP(3)) X SIMSEQ(0, N-1) X RouteID
= {0, 1, 2}
= {0, 1, .., N-1}
= {0, 1, ..}
L = {0, 1, ...}
L = {0, 1, ..., N-1}
L = {0, 1, ...}
Andrew Stone -- Colorado State University Slide 16
(lbl, sig) = rhs > lhs then phi else lhs
(lbl, sig) = lbl
(lbl, sig) = addtolist(lbl)

## Slide 17
BGP Policy
1 FMIntOp fmOp;
2 SimSeqOp seqOp;
3 LpOp lpOp;
4 LPInt prefRel;
5 SeqPref seqPref;
6 BGPRelationshipReader relationshipReader;
7 RouteIDReader routeIDReader;
8
9 // create the three algebras BGP is composed of
10 Algebra algFMLP(
"FMLP", &fmOp, &prefRel, &relationshipReader);
11 Algebra algAdd(
"SIMSEQ", &seqOp, &seqPref, &routeIdReader);
12 Algebra algRouteID(
"RouteID", &lpOp, &prefRel, &routeIDReader);
13
14 // calculate the composed routing algebra (the BGP
15 // policy). First parameter specifies number of
16 // algebras to compose
17 Algebra bgp = Algebra::lexProduct(
3, &algFMLP, &algAdd, &algRouteID);
Andrew Stone -- Colorado State University Slide 17

## Slide 18
Simulation Segmentation
All route's simulation has O(n^2) memory requirement
Swapping kills performance
First just find routes to these nodes:
Then find routes to these nodes:
network | memory usage
1k nodes | 57 MB
10k nodes | 6.88 GB
30k nodes | could not test
internet (33k nodes) | could not test
Due to how we model the routing problem it is possible to do a set of simulations that each only solve the problem for a set of routes.
Andrew Stone -- Colorado State University Slide 18
Notes: Steve: How much HD space does this take?
Where does Internet graph come from?

## Slide 19
How set size affects memory usage
(simple policy)
Andrew Stone -- Colorado State University Slide 19

## Slide 20
How set size affects performance
(simple policy)
Andrew Stone -- Colorado State University Slide 20

## Slide 21
Shared Memory Scalability
Andrew Stone -- Colorado State University Slide 21
Chart: Number of threads
Actual | 1 | 1.42 | 1.53 | 2.48
Ideal | 1 | 2 | 3 | 4

## Slide 22
Shared Memory Scalability
Effective cache size is preventing ideal speedup
(cache per thread goes down as # of threads goes up)
Andrew Stone -- Colorado State University Slide 22

## Slide 23
Distributed Memory
Scalability
Andrew Stone -- Colorado State University Slide 23

## Slide 24
Conclusions
We've succeeded in our goal (43 min simulation on 10 machines)
Our tool:
Can input topologies via specification file
Includes a C++ framework based on metarouting
Can operate with BGP on internet topology
This tool is being used to conduct internet-routing research
Topologies are only going to get more complicated
We didn't get it on a shared memory architecture
(due to shared cache)
Do did get it on a distributed memory architecture
Scalability:
Andrew Stone -- Colorado State University Slide 24

## Slide 25
Questions?
Andrew Stone -- Colorado State University Slide 25